## Slide 1: Attitude and Orbit Modeling and Control
Sanny Omar

## Slide 2: Simulating a Satellite’s Orbit
The equations of motion for a thrusting spacecraft are simple
a is the acceleration of the spacecraft (in an inertial reference frame)
F is the summation of applied external forces
c is the engine exhaust velocity vector relative to the spacecraft
is the time rate of change of mass due to burning propellant
The equations of motion simplify to Newton’s second law if there is no change in mass over time
The acceleration can be numerically integrated to get velocity and position over time

## Slide 3: Orbital Perturbations and Out of Plane Effects
Comparison of disturbing acceleration for Earth orbits (Fortescue and Stark 1995)

## Slide 4: Gravitational Forces
Two-body gravity (spherical Earth) is the primary force in orbit
Gravitational perturbations exist due to the non-spherical shape of Earth
  Largest of these is J2 which is due to Earth’s oblateness
  Gravitational acceleration in the ECI frame with J2 is given by Bate, Muller and White as

## Slide 5: Mean Orbital Elements
Traditional osculating elements designed to describe two-body motion
These elements oscillate over an orbit due mainly to J2 perturbations (Earth’s oblateness)
J2 perturbations can be calculated for a given set of mean orbital elements
Perturbations added to mean orbital elements to get osculating elements
Analytical solution to quickly convert between the two
Better to use mean orbital elements if J2 perturbations are included

## Slide 6: Calculating Perturbations
Perturbations given in Vallado book (pg 649) as a function of the mean elements
  Note mean anomaly used instead of true anomaly

## Slide 7: Perturbations Cont.

## Slide 8: Mean Elements Performance

## Slide 9: Solar Gravity
Orbital elements of Earth around the Sun on Jan 1 2000, 1200 UTC
Earth orbital elements at desired time calculated based on Kepler’s laws
Earth position (Cartesian) calculated in heliocentric frame with orb_elems_to_eci function
  Axes of this frame aligned with ECI frame
  Vector from satellite to sun simply negative of vector from sun to Earth
  Acceleration due to solar gravity calculated by
If acceleration of satellite relative to sun is known and acceleration of Earth relative to sun is known, acceleration of satellite relative to Earth can be found.
 | (km) |  | (deg) | (deg) | (deg) | (deg)
Earth | 1.496E8 | .01671 | .00005 | -11.2 | 114.21 | -2.48
Earth | 1.496E8 | .01671 | .00005 | -11.2 | 114.21 | -2.48

## Slide 10: Lunar Gravity
Mean orbital elements of Moon around Earth on Jan 1 2000, 1200 UTC
Lunar orbital elements at desired time can be estimated based on Kepler’s laws
  Moon is perturbed by Solar gravity and Earth’s gravity so Keplerian orbit assumption is not good.
Lunar position (Cartesian) calculated in ECI frame
  Acceleration due to lunar gravity calculated by
 | (km) |  | (deg) | (deg) | (deg) | (deg)
Earth | 384400 | .0554 | 5.16 | 125.08 | 318.15 | 135.27
Earth | 384400 | .0554 | 5.16 | 125.08 | 318.15 | 135.27

## Slide 11: Numerical Integration
System must be expressed in state space form for numerical integration
State derivatives are a function of time and the current state
  Use ECI position and velocity as states
  Accelerations calculated from equations of motion
Once function written to compute state derivative from current state and time, MATLAB’s ode45 can be called to compute state over time

## Slide 12: MATLAB Orbit Propagator
% setting up the initial conditions and simulation parameters
radius = 6978;
grav_param = 398600
circ_vel = sqrt(grav_param/radius)
initial_pos_vel = [radius 0 0 0 4 circ_vel+1]' % all units in km
tspan = [0 100000]
options = odeset('RelTol',1e-9);
% definition of ode and numerical integration take place here
diffEq = @(time, init_pos_vel) [init_pos_vel(4:6); ...
-grav_param/norm(init_pos_vel(1:3))^3*init_pos_vel(1:3)];
[time, pos_vel] = ode45(diffEq, tspan, initial_pos_vel, options);
% Everything else in this function is related to plotting
hold on
[x,y,z] = sphere(100);
earth_rad = 6378;
surf(x*earth_rad, y*earth_rad, z*earth_rad);
plot3(pos_vel(:,1), pos_vel(:,2), pos_vel(:,3), 'g');
title('Uber Propagator');
xlabel('X Position (km)');
ylabel('Y Position (km)');
zlabel('Z Position (km)');

## Slide 13: Simulink Orbit Propagator
As with the MATLAB propagator, a control loop is needed that calculates and integrates the state derivative in terms of the current state
Scope block allow the user to view simulation parameters
function state_der = get_state_der(init_pos_vel)
grav_param = 398600;
state_der = [init_pos_vel(4:6); ...
-grav_param/norm(init_pos_vel(1:3))^3*init_pos_vel(1:3)];
end

## Slide 14: Programming Tips
MATLAB
  DO NOT put large chunks of code in one function or script
  Use as many small, modular functions as possible
    Each function should have only one specific purpose
  If you are copying and pasting a block of code that is more than one line long, you are doing something wrong
  Don’t hard code something that can be made a variable
  Use comments and descriptive variable names
Simulink
  Make all functional groups of blocks into subsystems
    Subsystems have inputs and outputs like regular blocks
  Store commonly used custom blocks and subsystems in a Simulink library and make simulations blocks link to the library
    When a change is made to the library block, all instances of that block change
  If you are copying and pasting a custom block and it is not a library link, you are doing something wrong

## Slide 15: Systems Tool Kit (STK)
STK is a system modeling and mission design software by AGI
Astrogator module can be used to define satellite orbits and plan maneuvers
  High Precision Orbit Propagator available
STK can compute access to ground station
STK can compute solar power generation
Interface between STK and MATLAB is available
STK can display the satellite in certain attitude configurations, but will not propagate attitude (as far as I know)

## Slide 16: Astrogator and Targeter
Astrogator’s targeter will use numerical optimization techniques to vary certain simulation parameters until a desired objective is met
  You must already have a good understanding of the system to use astrogator effectively
  You must know which parameters to vary and have good initial guesses
    Targeter may not converge otherwise
  Hohmann transfer using targeter demonstrated

## Slide 17: Kerbal Space Program
Game that allows player to build and launch rockets and space planes
Translational and rotational equations of motions numerically integrated when engines firing, attitude control actuators in use, or in planet atmosphere
Kepler’s laws and patched conics method used to determine trajectory when coasting in orbit
PD attitude control available
Gives a good intuitive feel of orbital mechanics and attitude dynamics

## Slide 18: Attitude Determination and Control Systems (ADACS)
Responsible for determining satellite orientation and pointing satellite correctly
Necessary to properly orient science, power, propulsion, and communication devices

## Slide 19: ADACS Sensors and Actuators
Reaction Wheels (3)
Magnetorquers (3)
Magnetometer (3-axis)
Rate Gyros (3-axis)
Sun Sensors
  Position Sensitive Detectors

## Slide 20: Coordinate Frames in ADACS Algorithms
Earth Fixed Inertial Frame – Origin at Earth center, x-axis toward vernal equinox, z-axis through North Pole
Orbital Frame – Origin at satellite cm, x-axis aligned with velocity, z-axis toward Earth
Satellite Body Frame – Origin at satellite cm and moves with the satellite

## Slide 21: Obtaining and using Direction Cosine Matrices (DCMs)
A direction cosine matrix transforms vectors from one frame to another
  The vector does not change (it is a physical quantity in space), only the way of describing it changes
A DCM transforming from frame A to frame B has column vectors which are the basis vectors of frame A expressed in frame B
The inverse of a DCM is it’s transpose and reverses the transformation

## Slide 22: Quaternions and Spatial Rotations
Quaternions rotate a vector by angle about an axis n within the same reference frame
The representation of the rotated vector in the original frame is identical to the representation of the original vector in a frame that has been rotated by angle about the axis n
Alternative definitions of quaternion arithmetic have been defined to make the frame rotation angle positive instead of negative
  Makes it very easy to make sign errors
We will work with the canonical quaternion definitions
y
x
x
y
Y’
X’
r
r'
r

## Slide 23: Quaternion Arithmetic
A Vector can be written as a quaternion with a zero scalar part
The conjugate of a quaternion () represents a rotation by about the same axis as the original quaternion
If frames A and B are initially aligned and frame B is rotated about axis n by angle and a quaternion q is created with this axis and angle, the representation of a vector r in frame B in terms of the representation in frame A can be calculated as
Note that this is the same vector obtained when r is rotated by about n and expressed in frame A

## Slide 24: Relative Quaternions and the Quaternion Derivative
Let the rotation from frame A to frame B be expressed by qb and the rotation from frame A to frame C be expressed by qc. We want to find the rotation from B to C (qbc).
The derivative of the quaternion specifying the orientation of a body fixed frame B relative to frame A (q) is given by

## Slide 25: Coordinate Frame Transformations
Direction Cosine Matrix
Quaternion
  Rotation vector () plus rotation about vector ()

## Slide 26: Attitude Dynamics
The state vector will consist of the 4 components of the quaternion specifying the orientation of the body frame with respect to the ECI frame, the 3 components of the angular velocity of the body frame with respect to the eci frame, and the wheel angular velocities
The angular accelerations (angular velocity derivatives) can be found using the rotational form of Newton’s second law and the transport theorem. Let N denote the ECI frame and B the body frame.
This equations states that the summation of external moments is equal to the time rate of change of system angular momentum. For a rigid body
If using reaction wheels, add angular momentum of each wheel to body angular momentum

## Slide 27: De-Tumble Algorithm
B-Dot de-tumble algorithm
  Minimize angular velocity by torqueing opposite to direction of angular velocity vector

## Slide 28: Attitude Determination Vectors
Requires knowledge of two vectors in both coordinate frames
  Sun vector in body frame from sun sensors
  Magnetic field vector in body frame from magnetometer
  Magnetic field vector in orbital frame from IGRF model
  Sun vector in orbital frame from heliocentric orbit propagator
  Angular velocity vector (in body frame) from rate gyros

## Slide 29: Attitude Determination
Defined as direction cosine matrix between orbital frame and body frame
Triad algorithm gives DCM based on two vectors known in both frames
A is the direction cosine matrix
DCM to quaternion conversion

## Slide 30: Kalman Filtering
A Kalman Filter is an Optimal Estimator if a measurement contains Gaussian noise
Sensor measurements should be filtered before being used in ADACS algorithms

## Slide 31: Error Quaternion
Relates current orientation (qm) to desired orientation (qd)
  Used in control algorithm
  Quaternions are specified rotating the orbital frame to the body frame

## Slide 32: Legacy PD Control Algorithm
Torques calculated directly from controller
  Controller does not take wheel angular momentum into account
    System response changes with wheel angular velocity
    Can result in unexpected performance
    Controller gains dependent on satellite inertia properties
  Separate gain value needed for each parameter

## Slide 33: Inverse Dynamics PD Controller
Takes satellite dynamics into account
  Ensures stability in all conditions
PD law determines desired angular accelerations
Equations of motion used to calculate required torques
Gains independent of inertia properties

## Slide 34: Analytical Calculation of Controller Gains
Controller is quasi-linear, so block diagram can be drawn and used to calculate gains for linearized controller
Critically Damped:
Underdamped:
Overdamped:

## Slide 35: MATLAB Attitude Propagator
The state vector will consist of the 4 components of the quaternion specifying the orientation of the body frame with respect to the ECI frame, the wheel angular velocities, and the 3 components of the angular velocity of the body frame with respect to the ECI frame
Quaternion derivatives found based on current quaternion and angular velocity
Wheel angular accelerations found based on control law
Satellite angular acceleration based on system dynamics
Numerically integrate the state derivative to get evolution of state over time

## Slide 36: Simulation Results
Controller Simulation in MATLAB
  System behavior independent of inertia properties
rad/s

## Slide 37: Adams Results
Critically Damped Case (Kp=1, kd=-1.4)
Underdamped Case (Kp=1, kd=-.5)
Overdamped Case (Kp=1, kd=-4)

## Slide 38: Simulink Attitude Propagator

## Slide 39: MSC Adams Software
Software for multibody dynamics simulation
Contains primitive CAD software to specify mechanical bodies and connections between them
Can handle flexible body dynamics with many degrees of freedom
Student licenses available from MSC Software free of charge

## Slide 40: Office Hours and Contact Information
Sanny Omar
  email: sanny.omar@gmail.com
Office hours (MAEA-211):
  Monday 10-11:30 am
  Wednesday 9-10:30 am